## Slide 1: Storage Virtualization

## Slide 2: Changing The Network Architecture
Agility
Time
Network Virtualization
Consolidation
Improved Utilization, Efficiency
Automation
Policy-based Adaptive Infrastructure
Virtualization
Improved Flexibility, Responsiveness
Application Virtualization
Semi-Automated Provisioning
Data Center Consolidation
Dynamic Service Automation
Storage Virtualization
Server Virtualization
Static Provisioning
Branch Infrastructure Consolidation
Server Consolidation
Storage Consolidation
Notes: 2
2
Now, obviously customers are not going to get there in one fell swoop. And we see them moving from -- through a journey. And our job is to help them through that journey. They usually start with consolidation. That's the first aspect they realize in moving forward to do data centers. Whether it be looking out at the branch office environments and using WAAS technology to pull those file systems back, or maybe even rolling out a huge storage network, some component leads them to drive a consolidation perspective.
Once they take that view, they're usually looking one step ahead in how they can virtualize and then optimize those type of services to really drive that TCO argument forward. But the more forward-thinking customers are starting to think about dynamic provisioning. So now how can I enable and scale the dimensions of this problem to be more agile to the business? We believe that this kind of approach and view demands an architectural perspective. If you build a foundation around consolidation and you don't take into account the future, you're never going to get there.
Maibel’s Notes
“state of the network slide”
Technically we have been in the virtualization business sisnce 1994
Virtualization is Changing Network Architectures -it is the only technology that in 15 years has changed the network architecture.
To date Cisco Data Center 3.0 has delivered
  Delivered VM Networking
  Balanced Virtualization with Scalability, Reliability, and Security
  Homogenized the I/O from the server
  Enabled Any Workload on Any Server Anywhere
  Moved from Hardware Provisioning to Software Provisioning in the Data Center
  Purpose-Built Data Center Platforms
Cisco has Built the Unified Fabric for the Data Center

## Slide 3: Objectives
Identify the roles of Storage Virtualization
Review some terms and issues related with Storage Area Network (SAN)
State the benefits VSAN, N-Port Virtualizer and FlexAttach

## Slide 4: Storage Virtualization
Front-End
Virtual SANs/Unified IO
Virtual Storage
Virtual Network Services
Virtual Firewall Context
1
Virtual
SSL Context
3
Virtual Machines
Front-End Virtualization
Virtual Firewall Context
1
Virtual Firewall Context
1
Virtual
SLB Context
29
Virtual
SSL Context
3
Virtual
SSL Context
175
VSS
VLAN
VRF
VPNs
VDC
vHBA
VSANs
FCoE
CNA
Back-End
Refers to providing a logical, abstracted view of physical storage devices.
Provides a way for many users or applications to access storage without being concerned with where or how that storage is physically located or managed.
Pooling of physical storage from multiple network storage devices into what appears to be a single storage device that is managed from a central console.
Helps the storage administrator perform the tasks of backup, archiving, and recovery more easily, and in less time, by disguising the actual complexity of the SAN.

## Slide 5: SANs Attributes and Fabric Zoning
Factors to be considered when designing and deploying (SANs): High availability, scalability, and security of the network
Fabric zoning is a fundamental feature in today’s Fibre Channel switching products.
Zoning provides a means of restricting visibility and connectivity between devices connected to a common Fibre Channel SAN.
While zoning provides a basic security function within a fabric, it does not provide any enhancements in terms of the scalability and availability of the fabric.

## Slide 6: Cisco Virtual SANs
Cisco Virtual SANs enhances fabric scalability and availability, and further augment the security services offered by fabric zoning.
VSANs is implemented within the Cisco MDS 9000 Family of Multilayer directors and fabric switches.
VSANs combined with hardware-enforced zoning provide the SAN designer with new tools to highly optimize SAN deployments in terms of scalability, availability, security and management.

## Slide 7: Virtual Storage Area Network Deployment
Consolidation of SAN islands
Increased utilization of fabric ports with just-in-time provisioning
Deployment of large fabrics
Dividing a large fabric in smaller VSANs
Disruptive events isolated per VSAN
RBAC for administrative tasks
Zoning is independent per VSAN
Advanced traffic management
  Defining the paths for each VSAN
  VSANs may share the same EISL
  Cost effective on WAN links
Resilient SAN extension
Standard solution (ANSI T11 FC-FS-2 section 10)
SAN Islands
Department A
Department B
Department C
Virtual SANs
(VSANs)
Department A
Department B
Department C

## Slide 8: VSAN Advantages for Consolidation
OLTP
SAN Islands
Overlay Isolated Virtual Fabrics (VSANs) on Same Physical Infrastructure
E-Mail
Backup
Backup VSAN
E-Mail VSAN
OLTP VSAN
Consolidated SANs
Attribute |  | 
More | Number of SAN Switches | Fewer
No | Share Disk/Tape | Yes
No | Share DR Facilities | Yes
Complex | SAN Management | Simple
Very hard | Support Virtualization and Mobility | Easy

## Slide 9: VSAN Technology
Hardware-based isolation of tagged traffic belonging to different VSANs
Create independent instance of fiber channel services for each newly created VSAN
Fibre Channel Services for Blue VSAN
Fibre Channel Services for Red VSAN
Fibre Channel Services for Blue VSAN
Fibre Channel Services for Red VSAN
Cisco MDS 9000 Family with VSAN Service
VSAN Header Is Added at Ingress Point Indicating Membership
No Special Support Required by End Nodes
Trunking E_Port (TE_Port)
Trunking E_Port (TE_Port)
Enhanced ISL (EISL) Trunk Carries Tagged Traffic from Multiple VSANs
VSAN Header Is Removed at Egress Point
The Virtual SANs Feature Consists of Two Primary Functions

## Slide 10: Inter VSAN Routing
Similar to L3 interconnection between VLAN
Allows sharing of centralized storage services such as tape libraries and disks across VSANs—without merging separate fabrics (VSANs)
Network address translation allow interconnection of VSANs without a predefined addressing schema
Tape VSAN_4 (Access via IVR)
VSAN-Specific Disk
Engineering VSAN_1
Marketing VSAN_2
HR VSAN_3
IVR
IVR

## Slide 11: N_Port_ID & WWN
An N_Port is an end node port on the Fibre Channel fabric. This could be an HBA (Host Bus Adapter) in a server or a target port on a storage array. An N_Port is connected to an F_Port on a Fibre Channel switch.
Normally, an N_Port would have a single N_Port_ID associated with it. An N_Port_ID is a 24-bit address assigned by the Fibre Channel switch during the FLOGI process. For any given physical N_Port, there would be exactly one WWN (World Wide Node Name) and one N_Port_ID associated with it.
Application Server
FC Switch
Web I/O
N_Port_ID
F_Port

## Slide 12: N-Port ID Virtualization (NPIV)
Mechanism to assign multiple N_Port_IDs to a single N_Port
Allows all the access control, zoning, port security (PSM) be implemented on application level
Multiple N_Port_IDs are allocated in the same VSAN
Application Server
FC Switch
E-Mail
Web
File Services
Email I/O
N_Port_ID 1
Web I/O
N_Port_ID 2
File Services I/O
N_Port_ID 3
F_Port

## Slide 13: Summary
VSANs provide the ability to create completely isolated fabric topologies, each with its own set of fabric (including zoning) services, on top of a scalable common physical infrastructure.
NPIV provides a means to assign multiple FC IDs to a single N port, and allows multiple applications on the N port to use different identifiers. NPIV also allows access control, zoning, and port security to be implemented at the application level.
NPV addresses the increase in the number of domain IDs needed to deploy a large number of the ports by making a fabric or module switch appear as a host to the core Fibre Channel switch, and as a Fibre Channel switch to the servers in the fabric or blade switch.
Cisco FlexAttach allows administrators the flexibility to add, move, or replace servers easily without the need to reconfigure SAN switches or storage arrays.